## Slide 1: EE281 (Introduction to Electrical Engineering II) and EE285 (Electronics I) BJT Amplifier Configurations
Dr. Melaka Senadeera
Department of Electrical and Electronics Engineering
University of Peradeniya
Peradeniya

## Slide 2: Transistor configurations
Transistor configurations
  Common base (CB) configuration
  (No current gain, but voltage gain)
  Common collector (CC) configuration
  (Current gain, but no volatge gain)
  Common Emitter (CE) configuration
  (current gain and voltage gain)

## Slide 3
Transistor configurations
  Base terminal common to both input and output
  The input is applied between the base and emitter
  terminals and the corresponding output signal is
  taken between the base and collector terminals with
  the base terminal grounded
  Input parameters are VEB and IE and the output
  parameters are VCB and IC.
Notes: 333

## Slide 4
Transistor configurations
Voltage gain for this configuration
AV = Vout/Vin = (IC*RL) / (IE*Rin)
Current gain in common base configuration
α = Output current/Input current
α = IC/IE
Notes: 444

## Slide 5
Transistor configurations
Input Characteristics
Input characteristics are obtained between input current and input voltage with constant output
voltage.
Keep the output voltage VCB constant and vary the input voltage VEB for different points then at
each point record the input current IE value.
Repeat the same process at different output voltage levels.
Rin = VEB / IE (when VCB is constant)
Notes: 555

## Slide 6
Transistor configurations
Output Characteristics
The output characteristics of common base configuration are obtained between
output current and output voltage with constant input current.
Keep the emitter current constant and vary the VCB value for different points, record the IC values at each point.
The equation to calculate the output resistance value is given below.
Rout = VCB / IC (when IE is constant)
Notes: 666

## Slide 7
Transistor configurations
  Emitter as common terminal for both input and output
  Common emitter configuration is an inverting amplifier
  circuit.
  Input is applied between base-emitter region and the
  output is taken between collector and emitter terminals
  input parameters are VBE and IB and the output
  parameters are VCEand IC.
  The input is applied between the base and emitter
  terminals and the corresponding output signal is
  taken between the base and collector terminals with
  the base terminal grounded
  Input parameters are VEB and IE and the output
  parameters are VCB and IC.
Notes: 777

## Slide 8
Transistor configurations
Current gains
Current gain (α) = IC/IE
Current gain (β) = IC/IB
Collector current IC =α IE = βIB
This configuration is mostly used one among all the three configurations.
It has medium input and output impedance values. It also has the medium current and voltage gains. But the output signal has a phase shift of 1800 i.e. both the input and output are inverse to each other.
Notes: 888

## Slide 9
Transistor configurations
The input characteristics
common emitter configuration are obtained between input current IB and input
voltage VBE with constant output voltage VCE.
Keep the output voltage VCE constant and vary the input voltage VBE for different
points
Draw a graph between the values of IB and VBE at constant VCE.
The equation to calculate the input resistance Rin is given below.
Rin = VBE/IB (when VCE is at constant)
Notes: 999

## Slide 10
Transistor configurations
Output Characteristics
Common emitter configuration are obtained between the output current IC and output voltage VCE
with constant input current IB.
Keep the base current IB constant and vary the value of output voltage VCE for different points.
Plot the graph between the parameters IC and VCE in order to get the output characteristics of
common emitter configuration.
The equation to calculate the output resistance from this graph is given below.
Rout = VCE/IC (when IB is at constant)
Notes: 101010

## Slide 11
Transistor configurations
  Collector terminal as common for both input and
  output signals.
  input signal is applied between the base-collector
  region and the output is taken from the emitter-
  collector region
  input parameters are VBC and IB and the output
  parameters are VEC and IE
Notes: 111111

## Slide 12
Transistor configurations
Current gain,
Ai = output current/Input current
Ai = IE/IB
Ai = (IC + IB)/IB
Ai = β + 1
Ai = (IC/IB) + 1
This common collector configuration is a non inverting amplifier circuit.
It has large current gain because the load resistor in this circuit receives both the collector and base currents.
Notes: 121212

## Slide 13
Transistor configurations
Input Characteristics
The input characteristics of a common collector configuration are quite different from the common base and common emitter configurations because the input voltage VBC is largely determined by VEC level. Here,
VEC = VEB + VBC
VEB = VEC – VBC
The input characteristics of a common-collector configuration are obtained between inputs current IB and the input voltage VCB at constant output voltage VEC. Keep the output voltage VEC constant at different levels and vary the input voltage VBC for different points and record the IB values for each point. Now using these values we need to draw a graph between the parameters of VBC and IB at constant VEC
Notes: 131313

## Slide 14
Transistor configurations
Output Characteristics
The operation of the common collector circuit is same as that of common emitter circuit.
The output characteristics of a common collector circuit are obtained
between the output voltage VEC and output current IE at constant input current IB.
In the operation of common collector circuit if the base current is zero then the emitter
current also becomes zero. ‘
As a result no current flows through the transistor
If the base current increases then the transistor operates in active region and finally reaches to saturation region.
Plot the graph between the parameters of IE and VCE at constant values of IB.
Notes: 141414

## Slide 15
Thank you
Notes: 151515