## Slide 1
LOW POWER COMPUTING
Topics
General Remarks Power and Energy Basic Techniques  Parallelism  VLIW (parallelism and reduced overhead)  Dynamic Voltage Scaling  Dynamic Power Management

## Slide 2
Power and Energy Consumption
Need for efficiency (power and energy): „Power is considered as the most important constraint in embedded systems.” [in: L. Eggermont (ed): Embedded Systems Roadmap 2002, STW] “Power demands are increasing rapidly, yet battery capacity cannot keep up.” [in Diztel et al.: Power-Aware Architecting for data-dominated applications, 2007, Springer]

## Slide 3
IMPLEMENTATION ALTERNATIVES

## Slide 4
POWER EFFICIENCY CONFLICT
Necessary to optimize HW and SW Use heterogeneous architectures Apply specialization techniques.

## Slide 5
Energy Efficiency

## Slide 6
Topics General Remarks Power and Energy Basic Techniques  Parallelism  VLIW (parallelism and reduced overhead)  Dynamic Voltage Scaling  Dynamic Power Management

## Slide 7
Power and Energy are Related
In many cases, faster execution also means less energy, but the opposite may be true if power has to be increased to allow faster execution.

## Slide 8
Low Power vs. Low Energy
Minimizing the power consumption is important for  the design of the power supply  the design of voltage regulators  the dimensioning of interconnect  cooling (short term cooling) • high cost (estimated to be rising at $1 to $3 per Watt for heat dissipation [Skadron et al. ISCA 2003]) • limited space Minimizing the energy consumption is important due to  restricted availability of energy (mobile systems)  limited battery capacities (only slowly improving)  very high costs of energy (solar panels, in space)  long lifetimes, low temperatures

## Slide 9
Power Consumption of a CMOS Gate

## Slide 10
Power Consumption of CMOS Processors
Main sources:  Dynamic power consumption • charging and discharging capacitors
 Short circuit power consumption • short circuit path between supply rails during switching
 Leakage • leaking diodes and translators • becomes one of the major factors due to shrinking feature sizes in semiconductor technology

## Slide 11
Dynamic Voltage Scaling (DVS)
Decreasing Vdd reduces P quadratically (f constant). The gate delay increases reciprocally with decreasing Vdd . Maximal frequency fmax decreases linearly with decreasing Vdd

## Slide 12
Example: Voltage Scaling

## Slide 13
Power Supply Gating Power gating is one of the most effective ways of minimizing static power consumption (leakage)  Cut-off power supply to inactive units/components  Reduces leakage

## Slide 14
Topics General Remarks Power and Energy Basic Techniques  Parallelism  VLIW (parallelism and reduced overhead)  Dynamic Voltage Scaling  Dynamic Power Management

## Slide 15
Use of Parallelism

## Slide 16
Use of Pipelining

## Slide 17
Topics General Remarks Power and Energy Basic Techniques  Parallelism  VLIW (parallelism and reduced overhead)  Dynamic Voltage Scaling  Dynamic Power Management

## Slide 18
New ideas help …